## Slide 1
Lecture 1
Heatsink Performance
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance
Spring 2026
423

## Slide 2
1
Heat Sink for a CPU Chip
Forced-convection cooling concept, thermal model, DFMA refinement, and validation plan.
Mission
Design a forced-convection heat sink that keeps a 100 W CPU below the official 85°C limit while evaluating a derated 70°C design target.
• Part 1: idealized 17-fin thermal baseline.
• Part 2: final 15-fin Al-6061 DFMA design.
• Prototype validation is required before real-world performance claims.
100 W
maximum chip power
85°C
official CPU limit
70°C
derated target
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance
423

## Slide 3
Official Problem Requirements
Requirement
Value
Design implication
CPU heat load
100 W
All resistance and temperature-rise calculations scale from this load.
Ambient air
25°C
Reference temperature for modeled heat rejection.
Official CPU limit
≤ 85°C
Pass/fail requirement for the project.
Derated target
≤ 70°C
Internal engineering target used for concept selection.
Validation
prototype test
Model and simulation must be checked against real hardware.
Course framing: design choices must be supported by simplified modeling, simulation evidence, and a test plan.
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance
423

## Slide 4
Convert the temperature requirements into a resistance scorecard.
Official limit
(85 - 25) / 100 = 0.600 °C/W
Requirement: CPU ≤ 85°C
Derated target
(70 - 25) / 100 = 0.450 °C/W
Target: CPU ≤ 70°C
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance

## Slide 5
Three Concept Options
Concept A
Copper Pin-Fin /
Natural Convection
Rejected: natural convection is insufficient for 100 W, and copper is heavy.
Concept B
Aluminum Folded-Fin
with Heat Pipes
Rejected: heat pipes improve spreading but add complexity, cost, and integration risk.
Concept C
Extruded Al-6061 Plate-Fin /
Forced Convection
Selected path: forced-convection plate fins best balance thermal performance, cost, and manufacturability.
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance

## Slide 6
Concept Selection Matrix
Original concepts are carried forward, then refined into the final DFMA plate-fin design.
Criteria
Copper Pin-Fin
Folded-Fin / Heat Pipe
17-Fin Plate
Thermal performance
Low for 100 W natural convection
Strong heat spreading
Best modeled cooling
Manufacturability
Heavy copper machining
Complex assembly
Tight ideal geometry
Airflow / spacing
Natural convection limited
Depends on pipe/fan packaging
Narrower spacing
Tool access / mounting
Heavy and awkward
More interfaces to mount
Less access margin
Mass / cost
High mass/cost
Higher cost
Cooler but higher mass
Prototype readiness
Reject
Reject
Thermal baseline only
Decision
REJECT
REJECT
BASELINE ONLY
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance
423

## Slide 7
17-fin Al-6061 plate-fin baseline
17-fin
61.487°C
Fusion 360 result under modeled boundary conditions.
61.487°C
Fusion 360 result under modeled boundary conditions.
Spring 2026
Engg 114 Heat Transfer
Lecture 1: Heatsink Performance

## Slide 8
Spring 2026
Engg 114 Heat Transfer
6

## Slide 14
Why the Ideal Design Needed Redesign
The cooler baseline had to become a buildable thermal system.
17-fin ideal baseline
• Cooler simulation result: 61.487°C
• Narrower spacing and less access margin
• Thermal-first geometry, not final product geometry
15-fin DFMA design
• MATLAB predicts 69.85°C
• Fusion 360 predicts 69.775°C
• 2.557 mm spacing improves airflow practicality and tool access
DFMA
REFINEMENT
Engineering decision: keep the 17-fin model as the thermal baseline, then select the 15-fin design as the manufacturable product direction.
Notes: Target time: 0:40. Use the transition line verbatim. Then explain the redesign reason: narrow spacing, tool access, mounting features, and real airflow make a thermal-only optimum incomplete. This slide is the handoff from classroom thermal resistance logic to DFMA design judgment.

## Slide 15
08
Notes: Target time: 0:55. Introduce Part 2 and the final selected geometry. The final 15-fin DFMA design has 2.557 mm spacing, an estimated 54.6 g mass, MATLAB predicted 69.85°C, and Fusion predicted 69.775°C. Stress that the design narrowly meets the 70°C target in simplified modeling and comfortably meets the 85°C official limit.

## Slide 16
PART 2 / FINAL DFMA
The final 15-fin design trades peak cooling for buildable margin.
08
ENGG 114 Heat Sink Review | modeled boundary conditions
FINAL 15-FIN DFMA DESIGN
15
fin count
2.557 mm
clear spacing
54.6 g
mass estimate
0.4485
R_total °C/W
69.85°C
MATLAB predicted
69.775°C
Fusion 360
• Open channels improve spacing and tool access.
• Notch/access penalty included in the simplified MATLAB model.
• Selected for spacing, lower mass, tool access, and manufacturability.
Notes: Target time: 0:55. Introduce Part 2 and the final selected geometry. The final 15-fin DFMA design has 2.557 mm spacing, an estimated 54.6 g mass, MATLAB predicted 69.85°C, and Fusion predicted 69.775°C. Stress that the design narrowly meets the 70°C target in simplified modeling and comfortably meets the 85°C official limit.

## Slide 17
MATLAB OPTIMIZATION
MATLAB places the selected design just inside the 0.45°C/W target.
09
ENGG 114 Heat Sink Review | modeled boundary conditions
SELECTED POINT
0.4485
°C/W R_total
69.85°C
predicted CPU
54.6 g
estimated mass
• Candidate sweep filtered resistance, spacing, and positive mass.
• The selected point lies narrowly inside the 0.45°C/W target.
• Optimization supports the DFMA choice; prototype testing remains required.
Notes: Target time: 1:00. Read the plot left to right. The black cloud is the broader candidate space, blue points are valid candidates, and the selected star sits just inside the 0.45°C/W target. The key professor-safe message is that the MATLAB sweep supports the 15-fin design, but the target margin is narrow.

## Slide 18
SENSITIVITY
The 70°C target is sensitive to airflow and contact resistance.
10
ENGG 114 Heat Sink Review | modeled boundary conditions
AIRFLOW ASSUMPTION
Baseline h = 65 W/(m²·K); weaker airflow can erase derated margin.
CONTACT RISK
+0.00155°C/W moves the model to about 70.00°C; +0.05°C/W gives about 74.85°C.
h = 65 W/m²K is an assumed convection coefficient, not proven fan performance.
Notes: Target time: 1:05. Explain the sensitivity risk. The h plot shows that airflow assumptions matter, while the TIM/contact plot shows how small added resistance can push the design to the 70°C boundary. The design still has margin to 85°C, but the derated target depends on contact quality and fan performance.

## Slide 19
DRAWING PACKAGE
Drawing package remains the key manufacturing gate.
11
ENGG 114 Heat Sink Review | modeled boundary conditions
• Show 50.8 mm footprint, fin count, height, thickness, spacing, base thickness, and notch geometry.
• Mass properties should reconcile to the 54.6 g MATLAB estimate.
• Mounting interface should verify existing hardware fit.
Notes: Target time: 0:40. State plainly that the final SolidWorks drawing package and mass properties were not found in the working folder. The placeholder is intentional. The drawing package should lock the geometry, notches, base, fin spacing, and mounting interface before manufacturing or prototype ordering.

## Slide 20
ENGG 114 Heat Sink Review | modeled boundary conditions
12
FUSION COMPARISON
Fusion 360 predicts these temperatures under modeled boundary conditions.
15-fin final DFMA design
Max = 69.775°C
Selected for spacing, lower mass, tool access, airflow practicality, and manufacturability.
17-fin ideal baseline
Max = 61.487°C
Thermally better, but retained as the baseline rather than the final manufacturable design.
Notes: Target time: 0:55. Compare the two Fusion outcomes. The 17-fin ideal baseline is cooler at 61.487°C, but the 15-fin final DFMA model is still at 69.775°C under modeled boundary conditions. This is the evidence bridge between the simplified MATLAB model and the CAD simulation result.

## Slide 21
ENGG 114 Heat Sink Review | modeled boundary conditions
13
VISUAL BOM / ASSEMBLY
Visual BOM shows final assembly components. Prototype/test hardware is listed separately.
1× Al-6061 15-fin heat sink
4× M3 screws /
standoffs
1× 50 mm
DC fan
1× thermal pad /
TIM
optional full
assembly render
Final Product BOM
Al-6061 15-fin heat sink | 50 mm fan | TIM / thermal pad | screws / standoffs / washers | fan guard if included
Prototype/Test BOM
100 W heater block | thermocouples | data logger | fan power supply | test fixture / insulation | safety items
Notes: Target time: 0:55. Present the BOM as two groups: final product parts and prototype/test hardware. Emphasize that a report-ready BOM should include vendor, part number, quantity, cost, and justification. In this deck, the table shows the needed line items and flags procurement details to finalize if not already in the report.

## Slide 22
ENGG 114 Heat Sink Review | modeled boundary conditions
13
Notes: Target time: 0:55. Present the BOM as two groups: final product parts and prototype/test hardware. Emphasize that a report-ready BOM should include vendor, part number, quantity, cost, and justification. In this deck, the table shows the needed line items and flags procurement details to finalize if not already in the report.

## Slide 23
`
ENGG 114 Heat Sink Review | modeled boundary conditions
13
Notes: Target time: 0:55. Present the BOM as two groups: final product parts and prototype/test hardware. Emphasize that a report-ready BOM should include vendor, part number, quantity, cost, and justification. In this deck, the table shows the needed line items and flags procurement details to finalize if not already in the report.

## Slide 24
TEST PLAN
Prototype testing closes the gap between simplified model and real hardware.
14
ENGG 114 Heat Sink Review | modeled boundary conditions
1
Assemble
Heat sink, TIM, fan, and mounting hardware
2
Instrument
CPU simulator, base, air inlet, and power
3
Run
100 W steady state near 25°C ambient
4
Compare
Measured R_total vs MATLAB/Fusion
5
Decide
≤85°C required; ≤70°C derated target
• Record steady-state chip/base temperatures and airflow condition.
• Use measured R_total = (T_chip - T_ambient) / 100 W.
• If measured result misses the 70°C target, adjust fan, TIM, or geometry before claiming margin.
Notes: Target time: 0:50. Use this slide to satisfy the prototype requirement. The test plan applies 100 W, records ambient near 25°C, measures steady-state temperatures, and compares measured R_total to MATLAB/Fusion predictions. The pass/fail logic is 85°C required and 70°C as the derated target.

## Slide 25
ENGG 114 Heat Sink Review | modeled boundary conditions
15
FINAL VERDICT
The 15-fin DFMA design is selected; the 17-fin design remains the ideal baseline.
The final 15-fin Al-6061 heat sink is selected because it balances modeled thermal performance with spacing, lower mass, tool access, and manufacturability. MATLAB predicts 69.85°C, and Fusion 360 predicts 69.775°C under modeled boundary conditions. The 17-fin ideal baseline is cooler at 61.487°C, but it is less practical for tool access and manufacturability. Prototype validation is required before real-world performance claims.
69.85°C
MATLAB predicted
69.775°C
Fusion 360 predicted
61.487°C
17-fin baseline
≤85°C
official requirement
Notes: Target time: 0:55. Deliver the verdict slowly and exactly. The final 15-fin Al-6061 design is selected because it balances the model results with DFMA concerns. Close by saying prototype testing is required for real-world validation, then invite questions so there is 2 to 3 minutes left for Q&A.

## Slide 26
ENGG 114 Heat Sink Review | modeled boundary conditions
17
PROFESSOR Q&A BACKUP
Answer with assumptions, margins, and required testing.
Why not choose 17 fins?
It is cooler, but the final 15-fin design gives better spacing, lower mass, tool access, airflow practicality, and manufacturability.
How close is the 70°C target?
MATLAB predicts 69.85°C and Fusion predicts 69.775°C under modeled boundary conditions.
What is the largest uncertainty?
The assumed convection coefficient h = 65 W/m²K and TIM/contact resistance; both must be checked during prototype testing.
What must the prototype prove?
At 100 W, measured CPU temperature must be ≤85°C; the 70°C target should be checked against real fan and interface conditions.
Notes: Backup only. Use if asked detailed professor questions. Keep answers conservative: modeled boundary conditions, simplified h assumption, contact resistance sensitivity, and prototype validation required.